## Slide 1: The Node Security Assessment
By John Freeborn

## Slide 2: Device Overview & Attack Surface
MCU: STM32F103C8T6
External SPI Flash: Winbond W25Q64JV
Exposed interfaces:
UART (USART2)
SWD debug header
SPI bus lines
Physical access assumed

## Slide 3: Finding 1: UART Debug Shell
Unauthenticated shell accessible at 9600 baud
Full access to internal debug commands
Enabled retrieval of initial flag
Real-world impact: privilege bypass

## Slide 4: Finding 2: Password Hash & Internal Flash
Extracted MCU flash via SWD
Hard‑coded password hash discovered
Hash cracked with wordlist attack
Sensitive data stored unencrypted

## Slide 5: Finding 3: External SPI Flash
Dumped W25Q64JV via Bus Pirate + flashrom
Found plaintext telemetry and stream data
No encryption or integrity protection

## Slide 6: Finding 4: Secret Stream
Probed outbound communication pins
Stream transmitted in plaintext over USART3
Revealed device identifiers & state
Vulnerable to eavesdropping/spoofing

## Slide 7: Conclusion
All five challenge flags successfully recovered
Major weaknesses:
  Unauthenticated debug interfaces
  Plaintext storage in MCU & SPI flash
  Unencrypted communication streams
Reinforces importance of secure‑by‑design in IoT systems